## Slide 1: MPEGTS简介

## Slide 2: 技术背景
分合流模块，播放dolby vision视频时，遇到卡顿，无画面等问题。
Ts 空数据包

## Slide 3: TS Packet Header
Ts数据包结构如下

## Slide 4: Program Association Table

## Slide 5: Program Map Table

## Slide 6: Stream Type

## Slide 7: Descriptors

## Slide 8: Descriptor Tags

## Slide 9: Registration Descriptor

## Slide 10: Private Data Descriptor

## Slide 11: ISO 639 Language Descriptor

## Slide 12: ISO 639 Information
https://en.wikipedia.org/wiki/List_of_ISO_639-2_codes
0x75 0x6E 0x64 -> und

## Slide 13: PID Table

## Slide 14: NULL Packet
Transport Stream packets may be null packets. Null packets are intended for padding of Transport Streams. They may be inserted or deleted by re-multiplexing processes and, therefore, the delivery of the payload of null packets to the decoder cannot be assumed.
For null packets the payload_unit_start_indicator shall be set to '0'.
PID value 0x1FFF is reserved for null packets (see Table 2-3).
In the case of a null packet the value of the transport_scrambling_control field shall be set to '00' (see Table 2-4)
In the case of a null packet the value of the adaptation_field_control shall be set to '01'.
In the case ofa null packet the value of the continuity_counter is undefined.
In the case of null packets with PID value 0x1FFF, data_bytes may be assigned any value. The number of data_bytes, N, is specified by 184 minus the number of bytes in the adaptation_field(), as described in 2.4.3.4 below

## Slide 15: Pmt Example
0x444F5649 ->DOVI

## Slide 16: Net Abstract Layer Unit (NALU)Type
 | VPS | SPS | PPS | IDR
Hevc | 0x40 | 0x42 | 0x44 | 0x26
H264 |  | 0x67 | 0x68 | 0x65